## Slide 1
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
NTDC Projects for which Financing is Required
Planning Power NTDC
March, 2014

## Slide 2
POWER DISPERSAL PROJECTS
1

## Slide 3
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Estimated EPC Cost (MUS$)
1- | Dispersal of Power from 6600 MW Imported Coal Based Plants at Gadani and 2200 MW Nuclear Power Plants near Karachi | 4432
2- | Evacuation of Power from Wind Power Projects at Jhimpir & Gharo Wind Clusters (1756 MW) | 86
3- | Evacuation of Power from 1000 MW Quaid-e-Azam Solar Park at Lal-Suhanra | 28
4- | 500 kV HVDC Transmission system between Tajikistan and Pakistan for Central Asia – South Asia Transmission Interconnection (CASA-1000) | 97
5- | Dispersal of Power From Patrind Hydro Power Project (147 MW) | 8
Summary of Power Dispersal Projects

## Slide 4
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Estimated EPC Cost (MUS$)
6- | Dispersal of Power From Dasu Hydro Power Project (Phase-II 1080 MW) | 432
7- | Dispersal of Power From Diamer Bhasha Hydro Power Project (4500 MW) | 1700
8- | Dispersal of Power From 1200MW Power Plant at Bin Qasim | 120
9- | Alliot Substation and Evacuation of associated HPPs (840MW) | 176
 | Total Added Generation Capacity ( 20323 MW) | 2679
Summary of Power Dispersal Projects

## Slide 5
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Scope of Work | Estimated EPC Cost (MUS$) | Expected Completion | Status of PC-I
1. | Dispersal of Power from 6600 MW Imported Coal Based Plants at Gadani and 2200 MW Nuclear Power Plants near Karachi | Phase-I | 1089.4 | 2017-18 | 50 copies forwarded to Planning Commission on 06-03-2014 for approval from ECNEC.
 |  | One 500 kV HVAC D/C T/L from Power Plants to 500 kV substation at Gadani (25 km) |  |  | 
 |  | 500 kV Collector Station at Gadani with 14 Line Bays. |  |  | 
 |  | ±600 kV HVDC Converter Station at Gadani and Lahore (4000 MW) with Electrode/Grounding stations. |  |  | 
 |  | ±600 kV Bi-polar HVDC Gadani-Lahore T/L (1000 km). |  |  | 
 |  | Phase-II | 2271.4 | 2017-18 | 
 |  | ±600 kV HVDC Converter Stations at Gadani & Faisalabad (4000 MW each) with Grounding stations. |  |  | 
 |  | ±600 kV Bi-polar HVDC T/L from Gadani to Faisalabad (1200 km). |  |  | 
 |  | 500kV Grid station at Lahore East and D/C T/Ls (2026km) |  |  | 
 |  | 500 kV Switching Station at Khuzdar, Ludewala, Ormara and Gawadar. |  |  | 
 |  | For Evacuation of 2x1100 MW Nuclear Power Plants near Karachi | 1227 | 2018-19 | 
 |  | Total | 4587 |  | 

## Slide 6
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Scope of work | Estimated EPC Cost (MUS$) | PC-I Status | Expected Completion
2. | Evacuation of Power from Wind Power Projects at Jhimpir & Gharo Wind Clusters (1756 MW) | 132 kV Jhimpir New Substation 132 kV Jhimpir New –TM Khan D/C T/L (82 km) 132 kV D/C T/L for interconnection of WPPs with 132 kV Jhimpir New (25 km) | 86 | PC-I forwarded to Planning Commission on 13.09.2013 | 2016-17
 |  | Upgradation of 132 kV Jhimpir substation to 220 kV substation with 3x250MVA (750 MVA)220/132 kV T/Fs 220 kV Gas Insulated Substation (GIS) at Gharo with 2x250 MVA (500 MVA) 220/132 kV T/Fs. 220 kV D/C T/Ls from 220 kV Jhimpir to existing 220 kV T.M. Khan Road substation (70 km). 220 kV double circuit transmission line from 220 kV Gharo to 220 kV Jhimpir substation (75 km). 132 kV double circuit transmission lines for interconnection of WPPs to Gharo (20 km). 132 kV double circuit transmission lines for interconnection of WPPs to Jhimpir (65 km). Addition of 3rd 450 MVA, 500/220 kV transformer at 500 kV Jamshoro. |  |  | 
 |  | 220 kV D/C T/L for in/out of Jamshoro –KDA S/C at 2x250 MW NBT Wind Power Plants (10 km) |  |  | 

## Slide 7
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Scope of Work | Estimated EPC Cost (MUS$) | PC-I Status | Expected Completion
3. | Evacuation of Power from 1000 MW Quaid-e-Azam Solar Park At Lal-Suhanra | Evacuation of First 100 MW Solar Power Plants (Phase-I): 132 kV double circuit transmission line on Rail conductor for interconnection of first 2x50 MW Solar Plants with the proposed 132 kV Bahawalpur – Lal-Suhanra S/C transmission line (4km). | 28 | PC-I approved by ECNEC on 12.02.2014. | 2015-16
 |  | Evacuation of 300 MW Solar Power Plants (Phase-II): 132 kV double circuit transmission line on Rail conductor for interconnection of 2x50 MW Solar Plants with proposed 132 kV Bahawalpur – Lal-Suhanra S/C at solar power plants (4km). 132 kV double circuit transmission line on Rail conductor for interconnection of 4x50 MW Solar Plants with proposed 132 kV Bahawalpur Cantt–Lal-Suhanra S/C transmission line (8km). 132 kV double circuit transmission line on Rail conductor from Bahawalpur New to Lodhran & looping In/Out of one circuit at 132 kV Baghdad-ul- Jaded Grid Station (40km). |  |  | 
 |  | Evacuation of 600 MW Solar Power Plants (Phase-III): 220 kV Grid Station at Lal-Suhanara with 3x250MVA, 220/132kV transformers along with allied equipment and accessories. 220 kV D/C transmission line on twin bundled Rail conductor from 220 kV Lal-Suhanra to 220kV Bahawalpur G/S (40km). Three 132 kV D/C transmission lines on Rail conductor from Solar projects sites to 220kV Grid Station at Lal-Suhanra (8km each). |  |  | 

## Slide 8
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Scope of Work | Estimated EPC Cost (MUS$) | PC-I Status | Expected Completion
4. | 500 kV HVDC Transmission system between Tajikistan and Pakistan for Central Asia – South Asia Transmission Interconnection (CASA-1000) | 500 kV Sub-station at Peshawar (250 km) | 97 | Forwarded to Planning Commission on 06-02-2014 for approval from ECNEC. | 2017-18
 |  | 500kV D/C T/L for In/Out of 500 kV Terbela-Peshawar S/C at 500 kV Peshawar New (15 km ) |  |  | 
 |  | In/Out of Two 220 kV Peshawar–Shahi Bagh D/C at Peshawar New (1+1 km) |  |  | 

## Slide 9
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Scope of Work | Estimated EPC Cost (MUS$) | Expected Completion | Status of PC-I
5. | Dispersal of Power From Patrind Hydro Power Project (147 MW) | 132 KV D/C T/L f rom Patrind HPP to Mansehra G/S (45 km) 132 KV D/C T/L for I/O of 132 kV D/C Patrind HPP to Mansehra G/S at Balakot ( 5 km) 132 KV D/C T/L for I/O of 132 kV D/C Patrind HPP to Mansehra G/S at Muzaffarabad II (5 km) | 8 | 2015-16 | 50 copies forwarded to Planning Commission on 07-03-2014 for approval from ECNEC.
6. | Dispersal of Power From Dasu Hydro Power Project ( 2160 MW) | Phase I Two 500 kV D/C T/L from Dasu to Palas Valley (35 km) Two 500 kV D/C T/L from Palas Valley to Mansehra (105 km) 500 kV D/C T/L from Mansehra to Islamabad West (100 km) | 456 | 2018-19 | PC-I is under preparation.
 |  | Phase II 500 kV D/C T/L from Mansehra to Faisalabad West with 40% series compensation (375 km) 500 kV Switching Station at Mansehra Extension at Islamabad and Faisalabad West | 432 | 2021-22 | 

## Slide 10
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Scope of Work | Estimated EPC Cost (MUS$) | Expected Completion | Status of PC-I
7. | Dispersal of Power From Diamer Bhasha Hydro Power Project (4500 MW) | 500 kV D/C T/Ls Basha I –Mardan new via Sawat Valley (337 km) Mardan New – Peshawar New (50 km) Basha I – Basha II (5 km) Basha II – Chillas (42 km) Chillas – Alliot (212 km) Alliot – Lahore (North) (330 km) 500 kV Substations 500 kV Substation Mardan 500 kV substation Lahore – North | 1700 | 2021-22 | PC-I will be prepared on finalization of load flow studies
8. | Dispersal of Power From 1200MW Power Plant at Bin Qasim | 500 kV double circuit transmission line from Bin Qasim Power Plant to Matiari 500 kV switching station approx. 180 km on quad bundle Greeley Conductor. Land and compensation Two 500 kV Line bays with shunt Reactors | 120 | - | PC-I will be prepared on finalization of load flow studies
9. | Alliot Substation and Evacuation of associated HPPs (840MW) | 500 kV D/C T/L from Suki Kinari to Alliot (100 km) Extension at Alliot substation | 176 | 2019-20 | PC-I will be prepared on finalization of load flow studies.

## Slide 11
NTDC’s SYSTEM STABILITY PROJECTS
11

## Slide 12
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Projects | Scope of work | Estimated EPC Cost (MUS$) | Expected Completion | Status of PC-I
1. | 500 kV Faisalabad West | Phase- II 500kV D/C T/L for In/Out of 500 kV Multan-Gatti S/C at 500 kV Faisalabad West (30 km) | 32.3 | 2016-17 | 50 copies forwarded to Planning Commission on 13-09-2013.
 |  | 220kV D/C T/L from 500 kV Faisalabad West to 220 kV Lalian New (80km) |  |  | 
2. | Extension/Augmentation of 500/220kV Rewat substation | Extension of 1x250 MVA 220/132 kV T/F | 7.04 | 2014-15 | 50 copies forwarded to Planning Commission on 13-09-2013.
 |  | Augmentation of 2x160 MVA 220/132kV T/Fs to 2x250MVA T/Fs |  |  | 
3. | 220 kV Chakdara (500 MVA at 220/132 kV ) | 220kV sub station with 2x250MVA 220/132 kV T/Fs and allied equipment. | 33 | 49.5 | 2015-16

## Slide 13
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Scope of work | Estimated EPC Cost (MUS$) | Expected Completion | Status of PC-I
4. | 500 kV Islamabad West (1500 MVA at 500/220 kV And 500 MVA at 220/132 kV) | 500/220kV sub station with 500/220kV 2x750 MVA & 220/132 kV 2x250MVA T/Fs and allied equipment. | 126 | 2017-18 | PC-I will be prepared on finalization of load flow studies.
 |  | In/Out of 500 kV Tarbela – Rewat S/C at Islamabad West (40+40km) |  |  | 
 |  | In/Out of 500 kV G/Barotha–Rewat S/C at Islamabad West (50+50 km) |  |  | 
 |  | In/Out of 220 kV Tarbela–ISPR S/C at Islamabad West (15km) |  |  | 
 |  | In/Out of 220 kV Mansehra/Islamabad University–ISPR D/C at Islamabad West (5+5km) |  |  | 

## Slide 14
NATIONAL TRANSMISSION AND DESPATCH COMPANY LIMITED
PLANNING POWER
Sr. No. | Name of the Project | Scope of Work | Estimated EPC Cost (MUS$) | Expected Completion | Status of PC-I
5. | Replacement of depleted material at existing grid stations of NTDC system | Replacement of obsolete/depleted equipment at 24 No. 500 & 220 kV grid stations. | 15.4 | 2015-16 | PC-I forwarded to Planning Commission on 13.09.2013 . Financing is proposed in ADB Tranche- III
6. | 220 kV Chakwal (500 MVA at 220/132 kV) | 220kV sub station with 2x250 MVA 220/132 kV T/Fs and allied equipment. (500 MVA) | 39 | 2016-17 | PC-I will be prepared on finalization of load flow studies.
 |  | In/out of 220 kV Mangla-Rewat S/C at Chakwal (60 km) |  |  |