## Slide 1: A Journey into Defensible Architecture: A Defenders’ Guide
Cybersecurity and Digitalization: Supply Chain Risks in the Electricity Sector

## Slide 2: Markus Mueller Principle Industrial Consultant Dragos
LinkedIn: www.linkedin.com/in/markusmuellerics
Email: mmueller@dragos.com
Website: www.dragos.com

## Slide 3: Brian Foster Senior OT Cybersecurity Architect Southern California Edison

## Slide 4: Reference Architectures Best Practices May Not Be The Best Approach
Define and segment the layers
Defense at each layer
Traffic inspection and filtering between layers
Encrypt critical data
Deploy security solutions on the network and endpoints
Zero Trust

## Slide 5: Reference Architectures Failure To Understand The Why Can Result In Failure

## Slide 6: Defensible Architecture A More Intelligent Approach
“Defendable Architecture: Achieving Cyber Security by Designing for Intelligence Driven Defense®” – Fitch & Mukin, Lockheed Martin Corp
  Explicitly design, implement, & maintain systems to support intelligence driven defense processes
Control #2 of SANS Five Critical Controls:
  Architectures that supports visibility, log collection, asset identification, segmentation, industrial DMZs, process-communication enforcement meets the definition.

## Slide 7: Intelligence Driven Defensible Architecture

## Slide 8: Implementing These Principles A small Utility

## Slide 9: ACME - Small The Start of the Journey
Sector: Utility
Subsector: Water\Wastewater
Employees: 76
Customers: 6000
Forecasted Growth: 150% YoY
Infrastructure
  7 Wells
  2 Large Water Tanks
  4 Small Water Tanks
  1 Treatment Plant
  2 Lift Stations
Technology Stack:
Business Systems
  O365
  Cloud Customer Information System (CIS)
OT Systems
  Rockwell PLCs
  Ignition Plant SCADA
  Badger Meter System - Automatic meter reading (AMR)

## Slide 10: ACME - Small The Catalyst
A business user clicked a link on a phishing email which resulted in:
  Downloaded Malware
  Infected and encryption of ~20 computers
  Impacted 2 operations systems
    Meter System
    Engineering Station

## Slide 11: ACME - Small Steps Taken
Crown Jewels Analysis
  Well 1 & Tank 1
  Treatment Plant
Threat Scenario Approach
  Opportunistic Ransomware
Identify Constraints
  Limited Budget
  Limited Staff
  Infrequent Production Outages

## Slide 12: ACME - Small Network Segmentation
Shared Infrastructure
IT/OT Separation

## Slide 13: ACME - Small Security Controls
System Hardening
  Password Vault
  Role Based Levels (Servers, Applications, PLCs)
    Admin
    Operator
    Read Only
FactoryTalk AssetCentre
  Secure Project Files
  Config Management
  Config Backup
MFA OT Remote and Admin
Backup Solution for OT
  Local NAS
  Offline Removable Disk

## Slide 14: ACME - Small Making it Defensible
Monitoring
  CMF
  SIEM
  Security Use Case
Intel Feeds
  WISAC
  OT-Cert
Playbooks
  IT/OT Disconnect
  OT Restoration
  Ransomware
Workforce
  Training
  OT/OPS
  Cross Training
Respond
  IR Tabletop Exercise
  Test Restore

## Slide 15: Implementing These Principles A Medium Utility

## Slide 16: ACME - Medium The Mid Point in the Journey
Sector: Utility
Subsector: Water\Wastewater & Electric
Employees: 254
Customers: ~9000
Forecasted Growth: 25% YoY
Infrastructure
  11 Wells\ 7 Tanks
  2 Treatment Plant
  3 Lift Stations
  4 Distribution Substations
  70 kV System
  12/21 kV System
Technology Stack:
Business Systems
  O365
  Cloud CIS\CRM\OMS
OT Systems
  Water SCADA
  Electric DMS
  Meter Systems
Communication
  Wireless
  Fiber
  Leased Cellular (Private APN)
  Leased Line

## Slide 17: ACME - Medium Steps Taken
Crown Jewels Analysis
  Water SCADA
  Electric SCADA
Threat Scenario Approach
  Opportunistic and Targeted Ransomware
  Hacktivism
Identify Constraints
  Limited Budget
  Limited Staff
  Infrequent Production Outages

## Slide 18: ACME - Medium Network Segmentation
Dedicated OT Infrastructure
One Up\Down Data Model
Internal Segmentation

## Slide 19: ACME - Medium Field Network

## Slide 20: ACME - Medium Identity Management

## Slide 21: ACME - Medium Security Controls
System Hardening
  Application Allowlisting
EDR
Privileged Access Management (PAM)
Backup Solution for OT
  Local\Site-to-Site Replication
  Offline to Tape

## Slide 22: ACME - Medium Making it Defensible
Monitoring
  ICS Network Visibility
  Hunts
Intel Feeds
  EISAC
Playbooks
  Compromised Credentials
  Compromised System
  Forensic Triage
Workforce
  SOC (MSSP)
Respond
  OT Tabletop Exercise
  Site Recovery Drill

## Slide 23: Implementing These Principles A Large(ish) Utility

## Slide 24: ACME - Large The Last Part of the Journey
Sector: Utility
Subsector: Water\Wastewater & Electric & Generation
Employees: 500
Customers: ~27,000
Forecasted Growth: 25% YoY
Infrastructure
  11 Wells\ 7 Tanks
  2 Treatment Plant
  3 Lift Stations
  6 Distribution Substations
  40 MW Solar & Wind Farm
  20 MWh BESS
  Distributed Solar\BESS
Technology Stack:
Business Systems
  Cloud CIS\CRM
  OMS
  GIS
OT Systems
  Water SCADA
  Electric ADMS
  AMI Meter Systems
Communication
  Wireless
  Fiber
  Private Cellular
  Leased MPLS

## Slide 25: ACME - Large Steps Taken
Crown Jewels Analysis
  ADMS
  Water SCADA
Threat Scenario Approach
  Ransomware
  APT
Identify Constraints
  Limited Budget
  Limited Staff
  Infrequent Production Outages
  Regulatory Oversight

## Slide 26: ACME - Large Network Segmentation
Micro Segmentation
Site Resilience
Path Resilience

## Slide 27: ACME - Large Field Network

## Slide 28: ACME - Large Identity Management

## Slide 29: ACME - Large Security Controls
Asset Management
Change Management
Baseline Tracking
Risk Based Vulnerability Management Program
Port Security
Hunt and Forensic Program
Backup Solution for OT
  Local\Cloud Replication
  Immutable Cloud Storage
  Standby Systems

## Slide 30: ACME - Large Making it Defensible
Monitoring
  Expanded ICS Network Visibility
  OT System Logging
  ICS Device Logging
Intel Feeds
  Information Sharing Groups
Playbooks
  Insider Threat
  Defensible Cyber Stance
Workforce
  SOC IT/OT (L2+)
  Responders
Respond
  Executive Tabletop Exercise
  System Recovery Drill

## Slide 31: Summary

## Slide 32: Defensible Architecture Summary

## Slide 33: Intelligence Driven Defensible Architecture Easy Right?
Understand how operations and business functions
Use an intel-driven design that fits the operation environment
Deploy technology and processes that support the ability to detect and respond to events
Develop resilience and response capabilities
Enabling and supporting defenders

## Slide 34
Thank You